1304 332 Unit Operation in Heat Transfer

Department of Chemical Engineering, Ubon Ratchathani University

Homework No.3 (New)

1. Air at 1 atm and 300K blows across a horizontal flat plate at a velocity of 33 m/s. The plate has constant surface temperature of 400K. Calculate the heat lost by the plate if the plate dimensions are 60 by 30 cm with the longer dimension in the direction of flow. Express in watts.

2. Engine oil enters a 1.25-cm-diameter tube 3 m long at a temperature of 38°C. The tube wall temperature is maintained at 65°C, and the flow velocity is 30 cm/s. Estimate the total heat transfer to the oil and the exit temperature of the oil.

Table 1 Properties of saturated liquids of Engine Oil (unused).

| T, °C | ρ kg/m3 | cp kJ/kg.°C | ν, m2/s | k W/m. °C | α, m2/s | Pr | β, K-1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 899.12 | 1.796 | 0.00428 | 0.147 | 0.911×10-7 | 47,100 | 0.70×10-3 |
| 20 | 888.23 | 1.880 | 0.00090 | 0.145 | 0.872 | 10,400 |  |
| 40 | 876.05 | 1.964 | 0.00024 | 0.144 | 0.834 | 2,870 |  |
| 60 | 864.04 | 2.047 | 0.830×10-4 | 0.140 | 0.800 | 1,050 |  |
| 80 | 852.02 | 2.131 | 0.375 | 0.138 | 0.769 | 490 |  |
| 100 | 840.01 | 2.219 | 0.203 | 0.137 | 0.738 | 276 |  |
| 120 | 828.96 | 2.307 | 0.124 | 0.135 | 0.710 | 175 |  |
| 140 | 816.94 | 2.395 | 0.080 | 0.133 | 0.686 | 116 |  |
| 160 | 805.89 | 2.483 | 0.056 | 0.132 | 0.663 | 84 |  |