1304 332 Unit Operation in Heat Transfer (1/2554)

Department of Chemical Engineering Ubon Ratchathani University

Home work No.11

1. An aqueous feed of 200 kg/h containing 25 wt % acetic acid is being extracted by pure isopropyl ether at the rate of 600 kg/h in a countercurrent multistage system. The exit acid concentration in the aqueous phase is to contain 4.0 wt % acetic acid. Calculate (a) the compositions and amounts of the exit extract and raffinate streams and (b) number of stages in countercurrent extraction. Use equilibrium data from table 1 as depicted below.

Table 1 Acetic Acid-water-isopropyl Ether System, Liquid-Liquid Equilibria at 293 K or 20°C

| Water layer (wt%) | Isopropyl Ether Layer (wt%) |
| --- | --- |
| Acetic Acid | Water | Isopropyl Ether | Acetic Acid | Water | Isopropyl Ether |
| 0 | 98.8 | 1.2 | 0 | 0.6 | 99.4 |
| 0.69 | 98.1 | 1.2 | 0.18 | 0.5 | 99.3 |
| 1.41 | 97.1 | 1.5 | 0.37 | 0.7 | 98.9 |
| 2.89 | 95.5 | 1.6 | 0.79 | 0.8 | 98.4 |
| 6.42 | 91.7 | 1.9 | 1.93 | 1.0 | 97.1 |
| 13.30 | 84.4 | 2.3 | 4.82 | 1.9 | 93.3 |
| 25.50 | 71.1 | 3.4 | 11.40 | 3.9 | 84.7 |
| 36.70 | 58.9 | 4.4 | 21.60 | 6.9 | 71.5 |
| 44.30 | 45.1 | 10.6 | 31.10 | 10.8 | 58.1 |
| 46.40 | 37.1 | 16.5 | 36.20 | 15.1 | 48.7 |